IMPORTANT CARBON MONOXIDE INFORMATION / UPDATES

FOR APARTMENT BUILDINGS WITH 3 OR MORE APARTMENTS:

Wisconsin Statutes now require the installation of Carbon Monoxide Detectors in existing buildings with 3 or more dwelling units with a fuel burning appliance.  (Comm. 62.1200)

Install an approved carbon monoxide detector in the following locations:

1. In the basement of the building if the basement has a fuel-burning appliance;

2. Within 15 feet of each sleeping area of a unit that has a fuel-burning appliance;

3. Within 15 feet of each sleeping area of a unit that is immediately adjacent to a     unit or room that has a fuel-burning appliance;

4. In each room not used as a sleeping area that has a fuel-burning appliance, the CO detector shall be installed within 75 feet of the fuel-burning appliance.

5. In each hallway leading from a unit that has a fuel-burning appliance, the C O detector must be installed within 75 feet of the unit.

FOR DUPLEXES AND SINGLE FAMILY DWELLINGS:

(Wisconsin Act 158 and WI Dept. of Commerce Rules)

Carbon Monoxide Detectors are required on each floor level including the basement.

On floors where there are bedrooms the detector needs to be within 21 feet of the doors to the bedrooms.  Refer to the manufacturer’s instructions for proper placement and installation.

NOTE:

There are no restrictions on height installation or power source. The disadvantage to pug-in detectors is that they take up valuable outlet space and can be removed easily by tenants.  Please consider those factors before installing pug-in models.

DEFINITIONS:

Fuel-burning appliance – means a device that is stalled installed in a building and burns fossil-fuel or carbon based fuel, where carbon monoxide  is a combustion by-product, including:  stoves, ovens, grills, clothes dryers, furnaces, boilers, water heaters, heaters and fireplaces.